## Slide 1: Wind power forecasting for the day-ahead energy market ENS Data Challenge 2020 Challenge Provider: Compagnie Nationale du Rhône Emile NAFFAH

## Slide 2: Project context

## Slide 3: Data challenge platform launched by the ENS (Ecole Normale Supérieure)
Easy to access supervised machine learning datasets
CNR is one of France’s leading renewable energy producers
Current challenge focuses on wind energy
ENS Data Challenge: A public data challenge platform with many interesting projects provided by top companies
https://challengedata.ens.fr/participants/challenges/34/

## Slide 4: Before we dive right in, a brief introduction to the electricity day-ahead market…

## Slide 5
The day-ahead electricity market
D
D+1
00h
00h
23h59
09h
Day-ahead forecast period
00h
Observed
Forecast
Provide forecast for D+1 at 09:00 of day D
Setting of the spot price (D+1 price) at 12pm
The day ahead electricity market is a bidding market;
All renewable energy producers must provide their production forecast for D+1 on day D;
Since electricity cannot be stored at a reasonable cost: Production = Consumption at every hour (balance)

## Slide 6
The day-ahead electricity market
D
D+1
00h
00h
23h59
09h
00h
Observed
Forecast
Provide forecast for D+1 at 09:00 of day D
Setting of the spot price (D+1 price) at 12pm
The day ahead electricity market is a bidding market;
All renewable energy producers must provide their production forecast for D+1 on day D;
Since electricity cannot be stored at a reasonable cost: Production = Consumptions at every hour (balance)
Day-ahead forecast period

## Slide 7
Why do we need to forecast production ?
Wind power producers
D
D+1
00h
00h
23h59
09h
00h
Observed
Forecast
Producers need to know how much they are going to produce for:
Power grid balancing
Optimizing energy sales (trading)

## Slide 8
Why do we need to forecast production ?
Wind power producers
D
D+1
00h
00h
23h59
09h
00h
Observed
Forecast
Errors in forecasting generate imbalance costs to the power grid
1
1

## Slide 9
Why do we need to forecast production ?
Wind power producers
D
D+1
00h
00h
23h59
09h
00h
Observed
Forecast
Errors in forecasting generate imbalance costs to the power grid
1
2
1
2
“Over production” is purchased at a less attractive price than the spot price

## Slide 10
Why do we need to forecast production ?
Wind power producers
D
D+1
00h
00h
23h59
09h
00h
Observed
Forecast
Errors in forecasting generate imbalance costs to the power grid
1
2
3
1
2
“Over production” is purchased at a less attractive price than the spot price
In case of “under production” the producer will have to pay a penalty (or negative price)
3

## Slide 11
Why do we need to forecast production ?
Wind power producers
D
D+1
00h
00h
23h59
09h
00h
Observed
Forecast
Errors in forecasting generate imbalance costs to the power grid
1
2
3
1
2
“Over production” is purchased at a less attractive price than the spot price
In case of “under production” the producer will have to pay a penalty (or negative price)
3
Accurate forecasts provide a high added value to the producer!

## Slide 12: The Challenge!

## Slide 13
Goal of the challenge: Forecast day-ahead production of 6 wind farms
WF1
WF6
WF3
WF2
WF5
WF4
This is a regression problem!
The benchmark to beat: Forecasts from CNR’s own operational models

## Slide 14: Let’s take a look at the data and see what we’re dealing with…

## Slide 15: Meteorological time-series from Numerical Weather Prediction Models
NWP4
NWP2
NWP3
NWP1
D-1
D+1
D
Run 00h D-1
Run 12h D-1
Run 00h D
Run 12h D
Run 00h D+1
Time of forecast 09h
Target
Data availability for the training set
Wind: U (zonal) and V (meridional) components
Temperature
Total cloud cover
https://www.college-de-france.fr/site/stephane-mallat/Challenges-2020.htm
Shape of data
Training set: hourly data from May 1st 2018 to January 15th 2019
For a given point on the grid

## Slide 16
NWP4
NWP2
NWP3
NWP1
D-1
D+1
D
Run 00h D-1
Run 12h D-1
Run 00h D
Run 12h D
Run 00h D+1
Time of forecast 09h
Target
Data availability for the test set
Meteorological time-series from Numerical Weather Prediction Models
https://www.college-de-france.fr/site/stephane-mallat/Challenges-2020.htm
Shape of data
Test set: From January 16th 2019 to September 20th 2019
Wind: U (zonal) and V (meridional) components
Temperature
Total cloud cover
For a given point on the grid

## Slide 17
NWP4
NWP2
NWP3
NWP1
D-1
D+1
D
Run 00h D-1
Run 12h D-1
Run 00h D
Run 12h D
Run 00h D+1
Time of forecast 09h
Target
Data availability for the test set
Meteorological time-series from Numerical Weather Prediction Models
https://www.college-de-france.fr/site/stephane-mallat/Challenges-2020.htm
Meteo forecasts are updated many times per day => At best, we have access to the weather forecasts generated 9 hours ago,
Hence, some meteo forecasts may be less accurate for some hours.
Wind: U (zonal) and V (meridional) components
Temperature
Total cloud cover
For a given point on the grid

## Slide 18
NWP4
NWP2
NWP3
NWP1
D-1
D+1
D
Run 00h D-1
Run 12h D-1
Run 00h D
Run 12h D
Run 00h D+1
Time of forecast 09h
Target
Data availability for the test set
Meteorological time-series from Numerical Weather Prediction Models
https://www.college-de-france.fr/site/stephane-mallat/Challenges-2020.htm
Meteo forecasts are updated many times per day => At best, we have access to the weather forecasts generated 9 hours ago,
Hence, some meteo forecasts may be less accurate for some hours.
Meteo data is provided at one grid point near the WF, thus the spatial aspect of the data is reduced (lack of spatial information),
Wind production may not be correlated to meteo data at this particular grid point;
In fact, wind production is highly sensible to spatial information (terrain) => Wind is a ressource that is highly local
Wind: U (zonal) and V (meridional) components
Temperature
Total cloud cover
For a given point on the grid

## Slide 19
NWP4
NWP2
NWP3
NWP1
D-1
D+1
D
Run 00h D-1
Run 12h D-1
Run 00h D
Run 12h D
Run 00h D+1
Time of forecast 09h
Target
Data availability for the test set
Meteorological time-series from Numerical Weather Prediction Models
https://www.college-de-france.fr/site/stephane-mallat/Challenges-2020.htm
Meteo forecasts are updated many times per day => At best, we have access to the weather forecasts generated 9 hours ago,
Hence, some meteo forecasts may be less accurate for some hours.
Meteo data is provided at one grid point near the WF, thus the spatial aspect of the data is reduced (lack of spatial information),
Wind production may not be correlated to meteo data at this particular grid point;
In fact, wind production is highly sensible to spatial information (terrain) => Wind is a ressource that is highly local
Observed power production in the training set corresponds to the observed total amount of energy injected by the WF in the grid over the entire hour
Whereas meteo forecasts are provided on instants.
Wind: U (zonal) and V (meridional) components
Temperature
Total cloud cover
For a given point on the grid

## Slide 20: My approach to the problem

## Slide 21: Methodology
Wind U component
Wind V component
Temperature
Datetime
Cloud cover
Wind speed
Wind direction
Temperature
Cloud cover
Month
hour
Input:
Raw data
Preprocessing
For each NWP
Boosted Regression Trees
Day-ahead forecast
Random Forest
Regression
Choice of regression models is based on the capacity of the model to capture non-linearity and model interactions between variables with minimal preprocessing (both models generate similar results)
Cubic effect of changes in wind speed
Wind power is a highly non-linear function of wind speed
A bit of physics first…
Cumulated Absolute Percentage Error

## Slide 22: Target response to main explanatory variables
Wind power curves are highly non-linear: Small error in wind = Significant error in power

## Slide 23: Can we accurately forecast wind power?

## Slide 24: Forecasts are smoother than observed production and sometimes fail to capture peaks and lows (due to spatial resolution and time resolution?) However, the forecasts are accurate!
WF1
WF2
WF3
WF4
WF5
WF6
Observed
Forecast

## Slide 25: There is still room for improvement!
Forecasting wind power is a real challenge:
It is necessary to rely on accurate weather forecasts;
We are limited by the delay between availability of the most recent weather forecast and the time of production forecast for some NWPs;
We have to keep in mind the fact that observed power production on hour H is the total cumulated amount injected into the grid throughout the entire hour, whereas the weather forecast is punctual;
Room for improvement:
Managed to beat CNR’s benchmark!
Currently ranked 19th out of 80 participants (10/12/2020),
Benchmark score: CAPE = 31.73%
My score: CAPE = 30.46%
On the data side
Spatial information and weather forecasts on a higher number of grid points around the WF may help provide better forecasts;
Include more weather variables (Humidity, Air pressure) that can impact air density;
Include planned maintenance events

## Slide 26: Thank you for your attention! Any questions?